## Slide 1: Vibration-Based Fault Detection Using Edge AI
Students:
  Văruicu Monica
  Cernătescu Andreea
  Sgaibă Cristian
  Popescu Mădălin

## Slide 2: Problem Statement
- Objective: Detect abnormal vibration patterns using edge-deployed AI models
- Edge AI Approach: 1D-CNN and SVM models optimized for TinyML and microcontroller constraints
- Implementation & Evaluation: IMU-based vibration data, TensorFlow Lite Micro inference, accuracy and latency analysis

## Slide 3: Motivation
- Cloud-based Processing: Introduces latency and relies on network connectivity
- Edge AI processing: Enables fast, local, and autonomous decision-making
- System Benefit: Reduced response time and improved real-time performance

## Slide 4: System Architecture
- Device: IMU (emulated)
- Edge: Local AI inference
- Cloud: Results analysis

## Slide 5: Device Layer
- Device: Microcontroller with integrated IMU vibration sensor (triaxial accelerometer)
- Real-world Reference: Arduino Nano 33 BLE Sense as representative embedded platform
- Project Approach: Physical hardware replaced by a real industrial vibration dataset

## Slide 6: Edge
- Local Data Processing: Signal segmentation, normalization, and feature preparation performed at the edge
- AI Inference: Execution of CNN and SVM models directly on edge devices
- Embedded Simulation: TensorFlow Lite used to emulate inference on microcontroller-class hardware

## Slide 7: Cloud
- Result Collection: Gathering inference outputs and system results
- Performance Analysis: Evaluation and comparison using performance metrics
- Conceptual Visualization: Reports and tables without a dedicated web dashboard

## Slide 8: Methodology
- Problem Formulation: Binary classification of mechanical system condition based on vibration signals (normal vs. fault)
- Signal Processing: Continuous vibration signals segmented into fixed windows of 256 samples, each treated as an independent instance

## Slide 9: Methodology
- Modeling approaches:
- CNN: Direct use of raw signal windows with automatic feature learning
- SVM: Manual feature extraction using time-domain (mean, RMS, kurtosis) and frequency-domain (FFT) features

## Slide 10: dataset
- Dataset: Real vibration signals collected under multiple mechanical operating conditions
- Operating States: Ideal and Wear (Normal), Cracking and Offset Pulley (Fault)
- Binary Labeling: Normal wear is tolerated, while critical mechanical faults require intervention

## Slide 11: Ideal & WEAR (Normal)
IDEAL
WEAR

## Slide 12: Cracking and Offset Pulley (fault)
CRACKING
OFFSET
PULLEY

## Slide 13: Implementation
- Software Pipeline: Fully implemented in Python with a modular structure for reproducible preprocessing, training, evaluation, and edge inference simulation
- CNN Implementation: TensorFlow-based model converted and int8-quantized using TensorFlow Lite to reduce model size and computational cost
- SVM Implementation: Linear SVM implemented with scikit-learn, selected for fair comparison and suitability for embedded deployment

## Slide 14: Results
- Int8 CNN: Accuracy ≈ 0.83 with ultra-low latency (~0.008 ms), suitable for real-time edge inference
- SVM: Accuracy ≈ 0.80 but significantly higher latency (~0.38 ms) due to feature extraction

## Slide 15: Results
- Key Insight: Similar accuracy but vastly different latency, critical for edge AI systems
- Model Comparison: Quantized CNN enables real-time edge deployment, while SVM is limited by feature extraction overhead

## Slide 16: Conclusions
- Overall Conclusion: Int8 quantized CNN offers the best trade-off between accuracy, latency, and complexity for TinyML applications
- Impact: Results demonstrate the feasibility of Edge AI for real-world industrial predictive maintenance based on vibration analysis